UDC 519.854.2

Pavlov a.a.,

sperkach m.o.

Tasks execution with a common due date on parallel machines with optimality criteria: total earliness minimization regarding the due date and the tasks' start time execution maximization

In the article the properties of the problem are researched to build a feasible schedule of tasks execution with a common due date for parallel machines with two simultaneous criteria of optimality: total earliness minimization regarding the due date and the tasks' start time execution maximization. The sufficient conditions of schedule's optimality are developed. The PDC-algorithm for the solution of the problem is given.

1. Introduction

The considered problem refers to the scheduling theory which methods are used to optimize the operational and production schedules. In particular, the given PDC-algorithm for this problem solution is the part of an algorithmware of the third level of the four-level hierarchical model for scheduling and operational planning [1].

2. Formulation of the problem

Given a set of jobs  (), number of machines , for a job  the processing time  is known. It is assumed that all jobs arrive at the same time and have a common due date , the processing of each job runs to completion without interruption of jobs. Processing jobs on each machine is continuous.

The goal is to construct a feasible schedule for jobs j ( J (which means all jobs are not tardy) in which the jobs start time r is maximum or the total earliness of jobs with respect to the due date is minimum. The earlier results for this problem are given in [2, 3, 4].

3. Investigation of the problem properties

Theorem. For a feasible schedule the two optimality criteria are equivalent: first is the most late start time of jobs processing, and the second is the minimization of the total earliness with respect to the common due date.

Proof. Consider an arbitrary feasible schedule . Denote  where  is processing time of the job  which is executed in th position on machine ;  is the number of jobs executed on machine .

Let  (figure 1).

Lemma. In a feasible schedule which is optimal by the first optimality criterion,  is the minimum possible.

Proof. Let’s denote  where  is the set of all feasible schedules.

In this case, in the feasible schedule  the maximum late start time of machines  equals to , and for any other feasible schedule this number can not be more.

In the schedule  (which is optimal by the first criterion) the total earliness is . Since , and  is minimum possible then the schedule  has the minimum possible total earliness. QED.

Corollary 1. An arbitrary feasible schedule  with  and the start time of machines  is optimal by the first and the second criteria.

Corollary 2. In [4] the optimality criterion for this problem is considered to maximize the start time of jobs processing on identical parallel machines with the common due date. For this criteria the sufficient signs of optimality of a feasible solution were obtained.

Let  (here  is the largest integer for which ),  (by definition ).

Then  () is theoretically the minimum time for which all units could execute all jobs if  (if ).

Fig. 1 – The schedule

Consider some schedule . Let’s introduce the notations:

is the completion time of all jobs on machine , ;

, ;

,  (further we will call  a reserve of machine  and  a lug of machine );

is a set of machines with ;

is a set of machines with ;

is a set of machines with  ;

is a set of jobs of schedule  which are executed on machine .

Given this notations, the objective function has the form:

.

Since the values of  and  do not depend on the ordering, maximizing start time  is equivalent to minimization of the maximum of the lugs .

We can show that there exists an optimal schedule that belongs to the schedule class .

Consider some of the properties of schedules .

Statement. For an arbitrary schedule  the following is true [3]:

= .

From this statement, taking into account the non-negativity of , follows that inequality  <  is impossible.

Let b is the greatest common divisor (GCD) of processing times of jobs . Let’s change the measurement units by dividing  by b. Furthermore, we assume that all  have GCD that equals to 1.

For a schedule  such mutually exclusive cases are possible.

Case I:  and , . In this case we have a schedule with uniform load of machines.

Case II:  and not for all   is true, in this case we have:

.

In this case, it’s possible to construct a schedule with uniform load of machines.

Case III: , in this case we have:

> .

In this case, it’s impossible to construct a schedule with uniform load of machines.

Let’s formulate signs of schedules’ optimality which we should seek to fulfill [2].

Sign of optimality 1.

A feasible schedule which has  and , , is an uniform and therefore optimal, since its  is minimum possible.

Sign of optimality 2.

A feasible schedule which has  and  for all , is optimal.

On the basis of signs of schedules optimality let’s define the set of permutations that will allow to consistently improve the criterion value.

In view of the Theorem, these sufficient signs of optimality are also sufficient signs of optimality of a feasible schedule for the criterion of minimization of the total earliness with respect to the common due date.

Corollary 3. For the criterion of maximization of the start time of jobs processing on identical parallel machines with the common due date the PDC-algorithm was given for the problem solution. This algorithm is also effective to solve the problem of the total earliness minimization with respect to the due date.

The Corollary 3 follows from the Theorem, Corollary 2 and the next Statement.

Statement. Let  is an arbitrary feasible schedule, and the time of machines start  is , and the total earliness  in this case equals to .

Then any permutation that transforms a feasible schedule  into a feasible schedule  for which:

- when , do not changes for  the total earliness value  (follows from the equality ).

- If  then  and, respectively, .

Consequently, all the permutations of PDC-algorithm [4] that improve the value of the first criterion are the improving permutations also for the second criterion.

The statement is proved.

Since the PDС-algorithm [4] implements only improving permutations, so, based on sufficient signs of optimality of feasible solutions, we define the set of permutations that will allow to consistently improve the criterion value and will be the basis for the developed polynomial part of the PDC-algorithm for the problem solution.

The permutations that improve schedules

To improve a schedule we need to focus efforts to the reduction of the maximal lug . For this we propose to use permutations of jobs between machines: when some subset of jobs from the machine  (denote it as , by definition ) is swapped with a subset of jobs from the machine  (denote this subset as , ). Let’s denote as  the difference between the sums of processing times of jobs that take part in the permutation:

.

Note that, as a result of such permutations applied to the current feasible schedule , in the new feasible schedule  for values  and  the following is true:

–  =  – .

Considering the conditions of execution and consequences, all permutations which lead to improving the schedule may be divided into four types that we will conventionally denoted as A, B, C, and D.

The generalized characteristics and properties of all kinds of permutations are shown in Table 1, and their detailed description is in the article [4].

The PDC-algorithm for the problem solution

On the basis of the signs of optimality and the developed set of permutations the algorithm is constructed for determining the maximum late start time of jobs in a feasible schedule on parallel machines with the common due date.

In [4] the detailed description of the algorithm is given. Let’s give its brief description.

In the article [3] a greedy algorithm is given for constructing the schedule  of the schedule class . This schedule can be taken as an initial one.

The scheme of the algorithm

STEP 1. To build the initial schedule , .

STEP 2. Define sets  and .

STEP 3. Checking the signs of optimality

IF any of the signs of optimality is true

THEN go to STEP 6 ( is optimal schedule).

STEP 4. Define the machine  corresponding to the maximum lug: .

STEP 5. For the machine , enumerating machines , execute a permutation of type A, B, or C.

IF such permutations are not found THEN

5.1. For the machine , enumerating all machines , execute a permutation of type D.

5.2. IF such permutations are not found

THEN go to STEP 6,

ELSE go to STEP 2.

ELSE go to STEP 2.

STEP 6. Define the maximum start time of jobs in the current schedule :   .

END of the algorithm

Table 1. The characteristics and properties of permutations

| Permutation type | Conditions of the permutation execution | Characteristics of the resulting schedule |
| --- | --- | --- |
| A | , |  |
| B | , |  |
| C | , |  |
| D | , |  |

Possible implementations of STEP 5:

- find the first permutation which improves the schedule and execute it;

- enumerate all possible permutations, find among them the most effective one and execute it.

The complexity of the algorithm is  where .

If for the resulting schedule  one of the signs of optimality is true then it is an optimal schedule. Otherwise, the objective function value of the schedule  is different from its optimal value by no more than  (if ) or  (if ).

4. Conclusion

The properties of the problem were researched to build a feasible schedule of tasks execution with a common due date for parallel machines with two simultaneous criteria of optimality: total earliness minimization with respect to the due date and the maximization of the jobs start time. It is proved that if the schedule is optimal for one of the criteria, it is automatically optimal also for the second criterion. The sufficient signs of schedules optimality are developed. The PDC-algorithm for the problem solution is given.

Bibliography

- Згуровский М.З. Минимизация лексикографического критерия для допустимого расписания на независимых параллельных приборах с произвольными директивными сроками [Текст] / М.З. Згуровский, А.А. Павлов, Е.Б. Мисюра // Вісник НТУУ “КПІ”. Серія «Інформатика, управління та обчислювальна техніка». – К.: “ВЕК+”, 2014. – №61. – с.4–17

- Pavlov A.A. The optimality signs of feasible solutions of intractable combinatorial optimization problems // Вісник НТУУ “КПІ”. Серія «Інформатика, управління та обчислювальна техніка». — К.: “ВЕК+”, 2013. – №59. — С.4–12.

- Павлов О.А. Поліноміальна складова ПДС-алгоритму розв’язання однієї задачі теорії розкладів / О. А. Павлов, О.Г. Жданова, О.Б. Місюра, М.О. Сперкач // Технологический аудит и резервы производства, 2013. — №6/3 (14). — С.47–52.

- Павлов О.А., Жданова О.Г., Сперкач М.О. Задача составления допустимого расписания с максимально поздним моментом запуска выполнения идентичными параллельными приборами работ с общим директивным сроком / О.А. Павлов, М.О. Сперкач, О.Г. Жданова // Вісник НТУУ “КПІ”. Серія «Інформатика, управління та обчислювальна техніка». – К.: “ВЕК+”, 2014. – №61 – С.93–102.

# Text boxes

machine